## Slide 1: GRIP: Scalable 3-D Global Routing using Integer Programming
Tai-Hsuan Wu, Azadeh Davoodi
Department of Electrical and Computer Engineering
Jeffrey Linderoth
Department of Industrial and Systems Engineering
University of Wisconsin-Madison
WISCAD VLSI Design Automation Lab http://wiscad.ece.wisc.edu
Notes: Title?

## Slide 2: Outline
Preliminaries
Global routing contributions
  Integer Program formulation
  Candidate route generation
  Subregion extraction / IP decomposition
Simulation results

## Slide 3: Global Routing: Problem Definition
v11
v12
v13
v14
v21
v22
v23
v24
v31
v32
v33
v34
v41
v42
v43
v44
cap. = C
v11
v33
v42

## Slide 4: Another View…
Benchmark adaptec1:
Contains 176K multi-terminal nets
Grid size – 324 x 324
Layers – 6

## Slide 5: Previous Works
Archer [Ozdal, ICCAD’07]
MaizeRouter [Moffitt, ASPDAC’08]
NTHU-Route 2.0 [Chang, ICCAD’08]
Fast Route 4.0 [Pan, ASPDAC’09]
Global Routing
Original formulation
[Nair, DAC’82]
Pattern Routing
History-based
IP/Lagrangian
Labyrinth [Kastner, TCAD’02]
DPRouter [Cho, ASPDAC’07]
BoxRouter 2.0 [Cho, ICCAD’07]
FGR [Roy, DAC’08]
SideWinder [Hu, SLIP’08]
2002
2003
2004
2005
2006
2007
2008
[Labyrinth]
[Hadsell and Madden]
[Westra et al.]
[Westra and Groeneveld]
[BoxRouter]
[Muller]
[BoxRouter 2.0]
[FastRoute]
[Archer]
[DPRouter]
[MaizeRouter]
[FGR]
[SideWinder]
[NTHU-Route 2.0]
[FastRoute 4.0]

## Slide 6: Shortcomings of Existing Approaches
Highly rely on a sequential ordering for routing the nets
Net decomposition
3-D Global Routing
(Without resource sharing)
(With resource sharing)
Horizontal edges
Vias
Vertical edges
global edges
global bins

## Slide 7: Our Contributions
IP Formulation
Price and Branch
Problem Decomposition
(parallel execution)
Scalable IP for GR
Global Routing
Price and Branch
Problem Decomposition
GRIP: Global Routing via
Integer Programming
Global Routing
In terms of all potential candidate routes for a net
Considers 3D routes directly
Systematic pricing approach to identify candidate routes
Decompose problem into “balanced” subproblems to improve runtime

## Slide 8: Integer Programming Formulation
S2
T2
S1
T1
(IP-GR)

## Slide 9: IP-GR: Features
Solves the 3-D Global Routing Problem directly
  Does not apply layer assignment and directly works on 3-D Steiner routes
  Minimizes wirelength and via cost simultaneously, and cost in general
Does not decompose into multi-terminal nets
Tends to route as many nets as possible without overflow
  Quickly gets rid of the dummy variables Si by assigning large penalty factor M

## Slide 10: Solving IP-GR: Motivation
S
T
Large number of decision variables (Steiner trees) for each net
S
T
3x3 bounding box: 12 routes
Routes go outside the bounding box?
Routes can go up and down
Solution: Pricing via Column Generation*!!
* “Decomposition principle for linear programs”, Operations Research 1960

## Slide 11: Our Contributions
IP Formulation
(handle 3-D GR)
Price and Branch
Problem Decomposition
(parallel execution)
Scalable IP for GR
Global Routing
Problem Decomposition
GRIP
IP Formulation
(handle 3-D GR)
Global Routing
Notes: reference

## Slide 12: Price and Branch Procedure
Create initial routes via pattern routing
Solve LP, get dual sol.
Identify new routes for each net
Setup edge weight
Have new routes?
Solve IP
yes
no
Pricing Phase:
Identify “promising” routes for each net
Solve IP-GR via branch and bound
Notes: Change font color

## Slide 13: Price and Branch Procedure
Create initial routes via pattern routing
Solve LP, get dual sol.
Identify new routes for each net
Setup edge weight
Have new routes?
Solve IP
yes
no
S2
T2
S1
T1
1.0
1.0
1.0
1.0
1.0
1.0
1.0
1.0
99.0
1.0
Notes: Solve the relaxed Linear Programming of IP-GR
Apply Column Generation to solve Linear Programming
  Only explicitly include a subset of possible routes which may reduce the objective value

## Slide 14: Identifying New Routes
Edge weights
  Quantity larger than or equal to 1 expressed based on the solution of the dual problem
  Relates to congestion of the relaxed problem and reflects the impact of all the candidate routes generated so far
  Used to identify new routes while capturing impact of all previously generated candidate routes
1.0
1.0
1.0
1.0
99.0
99.0
99.0
1.0
99.0
99.0
99.0
1.0
1.0
1.0
1.0
1.0
1.0
1.0
1.0
1.0
1.0

## Slide 15: Our Contributions
IP Formulation
(handle 3-D GR)
Price and Branch
Problem Decomposition
Scalable IP for GR
Global Routing
GRIP
IP Formulation
(handle 3-D GR)
Global Routing
Price and Branch

## Slide 16: IP Decomposition: Motivation
Big instance – too many rows in IP-GR
Solution: Problem Decomposition
Benchmark adaptec1:
Contains 176K multi-terminal nets
Grid size – 324 x 324
Layers – 6
# of Net constraints : 176K
# of Edge constraints : 629K
# of total constraints : 805K
+
=

## Slide 17: Solving IP-GR for A Subregion
S
auxiliary
node
T
T
0.0
0.0
Floating terminal

## Slide 18: Subregion Extraction / IP Decomposition
Procedure:
  Fix nets based on fast and approximate route generated by “Flute”*
  Recursively bi-partition the chip area into rectangles
    At each bi-partition balance “Average Edge Utilization”
  Go through the subregions in the order of their “Total Edge Overflow” and before solving a subregion detour as many inter-region nets as possible
adaptec1 3D benchmark
*“Flute: Fast lookup table based rectilinear steiner minimal tree algorithm for VLSI design.”, [Chu, TCAD’08]

## Slide 19: Detouring Inter-Region Nets
(Before detouring)
(After detouring)
1
2
3
4
5
6
7
8
9
10
11
12
Ordered in terms of their total edge overflow.
Notes: Need to replace figures

## Slide 20: Processing of Subregions with Limited Parallelism
Floating terminal
Fixed terminal
Traversed in terms of their total edge overflow.
1
2
3
4
5
6
7
8
9
10
11
12

## Slide 21: Further Improving Connection Between Subregions
Disconnect segments connecting rout fragments in adjacent subregions
Use similar IP formulation to reconnect boundary nets
Subregion 1
Subregion 2
0.0
0.0
0.0
0.0
0.0
0.0
0.0
0.0
0.0
0.0

## Slide 22: Simulation Setup
Column Generation procedure was implemented using MOSEK 5.0
CPLEX 6.5 was used to solve IP
All jobs were submitted to CS grid at UW-Madison using Condor
Evaluated 8 ISPD07’ benchmarks using the ISPD08 script
  Manually changed via cost in the script from 1 to 3 units
  Results in the paper were verified with an inaccurate version of the ISPD07 script
Benchmark | # of nets | Grid size | # of layers
adaptec1 | 176715 | 324x324 | 6
adaptec2 | 207972 | 424x424 | 6
adaptec3 | 368494 | 774x779 | 6
adaptec4 | 401060 | 774x779 | 6
adaptec5 | 548073 | 465x468 | 6
newblue1 | 270713 | 399x399 | 6
newblue2 | 373790 | 557x463 | 6
newblue3 | 442005 | 973x1256 | 6

## Slide 23: Comparison of Solution Quality (3D)
Benchmark | Best reported solution* |  |  | GRIP |  |  |  | 
 | OF | WL | Router | OF | WL | Edge Cost | Via Cost | %WL-impr.
adaptec1 | 0 | 88.59 | FGR | 0 | 81.0 | 36.4 | 44.5 | 8.57%
adaptec2 | 0 | 90.08 | FGR | 0 | 82.4 | 33.7 | 48.7 | 8.53%
adaptec3 | 0 | 200.59 | FGR | 0 | 185.4 | 97.5 | 87.9 | 7.57%
adaptec4 | 0 | 182.99 | FGR | 0 | 172.3 | 91.5 | 80.7 | 5.84%
adaptec5 | 0 | 260.18 | NTHU-R | 0 | 238.9 | 104.8 | 134.1 | 8.18%
newblue1 | 0 | 90.96 | NTHU-R | 0 | 83.9 | 24.9 | 59 | 7.76%
newblue2 | 0 | 132.54 | FGR | 0 | 121.4 | 48 | 73.4 | 8.41%
newblue3 | 31024 | 197.3 | NTUgr | 52518 | 156.1 | 76.2 | 79.9 | N/A
* Determined by looking at other reported results from the routers that have optimized for ISPD07 benchmarks using the 07 rules (via cost = 3)
GRIP can improve total wire length by about 7.84%
Solutions are available for download at http://wiscad.ece.wisc.edu/gr/

## Slide 24: GRIP Runtime Results (3D)
GRIP runs in 6 to 23 hours if limited parallelism is used.
Sequential runtime takes 1 to 23 days!
Ran on machines with at most 2G memory.
Selected time-consuming subproblems used only a fraction of 2G memory.
 |  | # of subregions | Runtime (min) |  | # Iterations | # Parallel executed subproblems | 
 |  |  | Wall Clock Time | Estimated Sequential Runtime |  |  | 
 |  |  |  |  |  | Ave. | Max
adaptec1 | 324x324 | 100 | 388 | 3118 | 12 | 8.3 | 18
adaptec2 | 424x424 | 169 | 455 | 5585 | 16 | 10.6 | 23
adaptec3 | 774x779 | 576 | 478 | 8776 | 32 | 18.0 | 38
adaptec4 | 774x779 | 570 | 509 | 8218 | 30 | 19.0 | 51
adaptec5 | 465x468 | 225 | 584 | 8168 | 16 | 14.1 | 30
newblue1 | 399x399 | 144 | 483 | 4086 | 18 | 8.0 | 15
newblue2 | 557x463 | 238 | 467 | 5151 | 23 | 10.4 | 18
newblue3 | 973x1256 | 1170 | 1430 | 28379 | 61 | 19.2 | 39

## Slide 25: Conclusions and Future Directions
GRIP achieves significant improvement in solution quality using Integer Programming without any tuning
We believe runtimes can be significantly improved with much more aggressive parallelism and independent solving of the subproblems
We plan to develop similar IP formulation and route generation to resolve overflows in ISPD08 benchmarks
We plan to extend route generation procedure to generate routes that are also optimized for delay

## Slide 26
Thank You
Notes: 26

## Slide 27: Comparison of Solution Quality (2D)
Benchmark | Best reported solution |  |  | GRIP |  |  |  | 
 | OF | WL | Router | OF | WL | Edge | Via | %WL-impr.
adaptec1 | 0 | 54.7 | FGR | 0 | 53.5 | 36.0 | 17.5 | 2.19%
adaptec2 | 0 | 52.4 | FGR | 0 | 51.3 | 33.3 | 18.0 | 2.10%
adaptec3 | 0 | 131.5 | FGR | 0 | 129.1 | 96.6 | 32.5 | 1.83%
adaptec4 | 0 | 125.0 | FGR | 0 | 123.4 | 90.2 | 33.2 | 1.28%
adaptec5 | 0 | 153.2 | FGR | 0 | 149.5 | 103.8 | 45.7 | 2.42%
newblue1 | 0 | 48.6 | NTHU-R | 0 | 47.7 | 25.2 | 22.5 | 1.85%
newblue2 | 0 | 76.5 | FGR | 0 | 75.0 | 48.4 | 26.6 | 1.96%
newblue3 | 31454 | 110.8 | NTHU-R | 50091 | 106.5 | 77.8 | 28.7 | -

## Slide 28: Column Generation – Pricing Problem
Solve the relaxed Linear Programming of ILP-GR
Apply Column Generation to solve Linear Programming
  Only explicitly include a subset of possible routes
Restricted Primal Problem:
Dual Problem:
Primal Solution
Dual Solution
If a route with
Then adding this route to the Restricted Primal Problem reduces the objective value

## Slide 29: Identify New Routes
T1
S1
e6
e28
How to identify a new route with ?
Create initial routes using pattern routing
Solve LP, get dual sol.
identify new routes for each net
Setup edge weight
Have new routes?
Solve ILP
yes
no