## Slide 1: A Parallel Integer Programming Approach to Global Routing
Tai-Hsuan Wu, Azadeh Davoodi
Department of Electrical and Computer Engineering
Jeffrey Linderoth
Department of Industrial and Systems Engineering
University of Wisconsin-Madison
WISCAD Electronic Design Automation Lab http://wiscad.ece.wisc.edu

## Slide 2: Overview of Global Routing
v11
v12
v13
v14
v21
v22
v23
v24
v31
v32
v33
v34
v41
v42
v43
v44
cap. = C
v11
v33
v42
Benchmark bigblue4:
More than 2M nets
Grid size – 403 x 405
Layers – 8

## Slide 3: GRIP*: Overview
IP Formulation
Price and Branch
Problem
Decomposition
GRIP
Global Routing
* [Wu, Davoodi, Linderoth--DAC09]

## Slide 4: GRIP: The IP Formulation
T2
T2
T1
T1
(ILP-GR)

## Slide 5: GRIP: Solution via Price-and-Branch
Price:
Solve linear program relaxation of (ILP-GR) using “column generation”
Branch:
Solve (ILP-GR) using S(Ti) instead of Ω(Ti)
Step 0: Start with S(Ti)={t1i}
Step 1: Solve linear program relaxation version of (ILP-GR) using current S(Ti)
Step 2: Based on solution of step 1, solve pricing problem for each net to identify new route t*
S(Ti) = S(Ti) U t*
Pass pricing condition?
Yes
S(T)
Step 2: Based on solution of step 1, solve a pricing problem for a net Ti to identify new route t*
Pass pricing condition?
Generates a set of promising candidate routes S(Ti)  Ω(Ti)
for each net Ti

## Slide 6: GRIP: Problem Decomposition
A subproblem is represented by
  A rectangular area on the chip
  A set of nets assigned to it
Subproblems should be defined to have similar complexity for: 1) workload balance, 2) avoiding overflow
GRIP’s strategy:
  Recursive bi-partitioning to define the subproblem boundaries
  Net assignment based on FLUTE* combined with dynamic detouring before solving each subproblem
adaptec1 3D benchmark
* [Chu, Wong--TCAD’08]

## Slide 7: GRIP: Solving the Subproblems
Floating
Fixed
1
2
3
4
5
6
7
8
9
10
11
12
0.0
0.0
0.0
0.0

## Slide 8: GRIP: Connecting Subproblems
Using IP-based procedure is essential to connect subproblems with low (or no) overflow
0.0
0.0
0.0
0.0
0.0
0.0
0.0
0.0
0.0
0.0

## Slide 9: GRIP: Results
Significantly high improvement in wirelength
  9.23% and 5.24% in ISPD2007 and ISPD2008 benchmarks, respectively
  Comparable or improved overflow in three unroutable benchmarks
However, even wall runtime (with the limited parallelism) prohibitively large
  6 to 22 hours on a grid with CPUs of 2GB memory

## Slide 10: PGRIP: Overview
Goal: Remove synchronization barrier between subproblems
  Allowing a much higher degree of parallelism without much degradation in wirelength or overflow
Subproblem 1
Subproblem 2
Subproblem n
IP-Based
“Patching”
Feedback to enhance connectivity
Partial routing solution

## Slide 11: PGRIP: 1) Subproblem Definition
Quickly generate a routing solution
  Solve relaxed version of (ILP-GR) after fixing some short nets using column generation
  (set to 10 minutes)
  Apply randomized rounding to get integer solution
Recursive bi-partition to define boundaries of rectangular subregions
  To get subproblems with similar complexity, it balances number of nets at each rectangle during bi-partitioning
  Stop when number of nets inside a subproblem is less than 4000
3. Traverse subproblems and apply some detouring to further enhance the net assignments
  In order of Total Edge Overflow similar of GRIP

## Slide 12: PGRIP: 2) Initial Subproblem Pricing
Procedure
  Apply pricing to solve each subproblem independently in a bounded-time (set to 5 minutes)
  Allow inter-region nets to connect to anywhere on the subproblem boundaries
When solving relaxed (ILP-GR), Qe set to be equal to the Manhattan distance of edge e from the center of the subproblem

## Slide 13: PGRIP: 3) IP-Based Patching
Patcher’s feedback
  Pseudo-terminal locations per boundary per inter-region net
  Goal is to define restricted window to enhance connectivity
T1
T2

## Slide 14: PGRIP: 3) IP-Based Patching
Subproblem 1
T1
T1
Subproblem 2
T2
T2
T1
T1
T2
T2

## Slide 15: PGRIP: 3) IP-Based Patching
Subproblem 1
T1
T1
Subproblem 2
T2
T2
T1
T1
T2
V’
e’
C11
C12
C13
C14
C21
C22
(ILP-Patch)
T2
C23
C24

## Slide 16: PGRIP: 3) Adjusted Pricing
Subproblems apply adjusted pricing
  Nets only allowed to connect within their provided spanning window per boundary
  (set to 20 minutes)
Branching is then used to solve the subproblems independently
T1
T2

## Slide 17: PGRIP: 4) Distributed Connecting of Subproblems
Subproblems are connected simultaneously (in parallel)
  Similar procedure as in GRIP
  Inside each subproblem, the remaining edge capacities are allocated uniformly among its boundary connection problems
c
c
c
c

## Slide 18: Simulation Setup
Pricing using MOSEK 5.0
Branching using CPLEX 6.5
All parallel jobs in CS grid at UW-Madison
  Machines of similar speed and same 2GB memory
Network managed by Condor
  Each CPU does one job at a time

## Slide 19: Simulation Setup
Runtime limits in PGRIP [target runtime: 75 minutes]
  Defining subproblems:10 minutes
  Initial pricing: 5 minutes
  Adjusted pricing: 20 minutes
  Branch-and-bound for solving subproblems: 10 minutes
  Pricing to connect subproblems: 20 minutes
  Branch-and-bound for connecting subproblems: 10 minutes

## Slide 20: Simulation Results: Comparison of QoS
 | PGRIP |  | GRIP |  | FGR |  | FR 4.0 |  | NTHU 2.0 | 
 | TOF | WL | TOF | WL(%) | TOF | WL(%) | TOF | WL(%) | TOF | WL(%)
a1 (07) a2 (07) a3 (07) a4 (07) a5 (07) n1 (07) n2 (07) n3 (07) | 0 0 0 0 0 0 0 41K | 82.3 83.4 186.5 173.2 241.5 84.9 123.3 156.3 | 0 0 0 0 0 0 0 52K | -1.56 -1.24 -0.58 -0.52 -1.07 -1.14 -1.55 -1.03 | 0 0 0 0 0 526 0 30K | 7.00 7.20 6.61 3.44 7.13 9.97 4.73 10.02 | 0 0 0 0 0 0 0 32K | 9.60 8.90 8.87 7.36 10.79 7.46 9.11 14.17 | 0 0 0 0 0 0 0 31K | 7.38 8.21 7.15 6.88 7.20 6.71 8.43 6.38
Average |  |  |  | -1.09% |  | 6.58% |  | 8.87% |  | 7.42%
n4 (08) n5 (08) n6 (08) n7 (08) b1 (08) b2 (08) b3 (08) b4 (08) | 132 0 0 54 0 0 0 176 | 124.9 223.8 172.0 338.4 54.0 86.5 126.5 221.1 | 152 0 0 74 0 0 0 186 | -0.44 -0.44 -0.88 -0.83 -0.54 -0.64 -0.24 -0.22 | 262 0 0 1458 0 0 0 414 | 3.65 3.95 4.61 3.37 5.81 5.38 4.20 4.54 | 144 0 0 62 0 0 0 152 | 6.78 5.47 5.83 5.17 6.72 9.50 3.24 8.50 | 138 0 0 68 0 0 0 162 | 4.29 3.38 2.78 4.22 3.49 4.50 3.22 4.30
Average |  |  |  | -0.53% |  | 4.44% |  | 6.40% |  | 3.77%

## Slide 21: Simulation Results: Runtime
 | PGRIP |  |  | GRIP |  | 
 | #Parallel | WCPU (min) | TCPU (min) | E[#Parallel] | WCPU (min) | TCPU (min)
a1 (07) a2 (07) a3 (07) a4 (07) a5 (07) n1 (07) n2 (07) n3 (07) | 90 110 211 221 280 122 215 258 | 76 76 77 79 77 76 77 82 | 2101 2704 6319 5221 3175 2306 4192 14590 | 8.3 10.6 18.0 19.0 14.1 8.0 10.4 19.2 | 388 455 478 509 584 483 467 1430 | 2247 2677 5168 5258 7133 3076 5228 6768
n4 (08) n5 (08) n6 (08) n7 (08) b1 (08) b2 (08) b3 (08) b4 (08) | 255 504 459 725 124 243 326 453 | 77 80 78 86 76 77 78 82 | 2944 4953 2219 4788 956 3411 2690 3096 | 8.5 9.5 8.9 9.0 3.9 8.0 7.3 7.6 | 529 821 448 985 339 690 731 726 | 3974 6598 5096 5377 2770 3793 3448 4400
Average | 287 | 78 | 4104 | 11 | 629 | 4563

## Slide 22: Conclusions & Future Works
Conclusions
  Removed synchronization barrier in GRIP
  High-level of distributed processing
  High use of IP—considered impractical for GR—shown to be practical when combined with distributed processing, allowing significant improvement in solution quality
Future works
  Explore use of pricing for quick congestion estimation
  Incorporate restrictive routing constraints within pricing, e.g. on net topology for delay consideration, metal usage for manufacturability

## Slide 23
Thank You
Notes: 23