## Slide 1: Power-Driven Global Routing for Multi-Supply Voltage Domains
Tai-Hsuan Wu, Azadeh Davoodi
Department of Electrical and Computer Engineering
Jeffrey Linderoth
Department of Industrial and Systems Engineering
University of Wisconsin-Madison
WISCAD VLSI Design Automation Lab http://wiscad.ece.wisc.edu
Notes: Title?

## Slide 2: Contributions
Interconnect power optimization for multiple supply voltage (MSV) domains
  power metric for global routing in MSV domains
  nonlinear Integer Program (IP) formulation with level converters
  approximation as a two-phase linear IP and parallel solving by IP decomposition

## Slide 3: Global Routing
cells
global edges
global bins
v11
v12
v13
v14
v21
v22
v23
v24
v31
v32
v33
v34
v41
v42
v43
v44
global edges
global bins
cap. = C

## Slide 4: Motivation
Interconnect power minimization
  reported to be around 30% of dynamic power for a 45nm high performance microprocessor*
  can significantly increase with wiring congestion and higher wire size at the higher metal layers
  one-time optimization in the design flow after (any combination) of placement and global routing
Why address at global routing?
  flexibility compared to detail routing
  metal layer and size known for each wire
  wire spacing can be approximated from utilization
*[R. Shelar and M. Patyra, ISPD 2010]

## Slide 5: Our Contributions
Power Model for GR
Power aware IP for GR
Problem Decomposition
MSV-based GR
Global Routing
Net decomposition based on supply voltage level
Estimate edge capacitance based on its utilization
Power aware IP for GR
Problem Decomposition
MSV-based GR
Global Routing

## Slide 6: Interconnect Modeling for MSV
cell
global bins
VL
level converter
VH
VH
VH
VL
VH
Each voltage island has either a low (VL) or high (VH) supply voltage
Place level converters (LCs) based on the terminal locations
Decompose a net which contains a LC into a set of sub-nets

## Slide 7: Interconnect Power Modeling*
Total interconnect power is estimated as where fclk is the frequency
Each net has corresponding switching activity αi, supply voltage Vi, the capacitances of its sink cell and its route
For route ti , the capacitance is the sum of the capacitances of the edges in ti
*[Shojaei, Wu, Davoodi, Basten, ISLPED 2010]

## Slide 8: GR Edge Capacitance Modeling
The capacitance of each GR edge is a function of the metal layer le, wire width we and wire spacing se :
where Ca and Cf are the area and fringe capacitances with respect to substrate, and Cc is the coupling capacitance
Cc
Cf
Ca
Substrate
Cc
Cf

## Slide 9: GR Edge Capacitance Modeling
Metal layer le is known for each GR edge, and we assume only one (minimum) wire width we at GR stage
The spacing se for an edge is estimated from the edge utilization re
Area, fringe, and coupling capacitances for metal layer 1 with respect to edge utilization for a 45nm library (i.e., NANGATE library)

## Slide 10: Our Contributions
Power Model for GR
Power Aware IP for GR
Problem Decomposition
MSV-based GR
Global Routing
Problem Decomposition
MSV-based GR
Global Routing
Power Model for GR

## Slide 11: IP for Wirelength Minimization*
S2
T2
S1
T1
*[Wu, Davoodi, Linderoth, DAC’09, TCAD’11]

## Slide 12: IP for Power Minimization
(PGR)

## Slide 13: PGR: Objective
Minimize total interconnect power directly in the objective
The switching activity αi and voltage level Vi are known (constant value) for each (decomposed) net
The capacitance of each GR edge is a variable, and will be determined during the optimization
  expressed as constraint
Penalize the unrouted nets by choosing a large M

## Slide 14: PGR: Capacitance Constraint
The unit capacitance of an edge typically is a piecewise linear convex function
For each line segment q, the edge capacitance can be written as without approximation
And the edge utilization is expressed as

## Slide 15: PGR: Wirelength Constraint
Rerouting nets from congested regions or to lower metal layers can reduce interconnect power
  but it may increase wirelength
Can control the tolerance parameter β to set an upper bound for the total wirelength

## Slide 16: Our Contributions
Power Model for GR
Power Aware IP for GR
Problem Decomposition
MSV-based GR
Global Routing
Two-phase approach to reduce complexity of IP
Decomposition into sub-problems
Power-aware route generation
Power Aware IP for GR
MSV-based GR
Global Routing
Power Model for GR

## Slide 17: PGR Complexity
(PGR)
All the constraints in PGR are linear but the objective expression is nonlinear
Utilize a two-phase approach to handle the nonlinearity
  Phase1: Minimize total capacitance by rerouting nets, and obtain the estimation of edge capacitance
  Phase2: Fix capacitance and consider net activity and voltage level

## Slide 18: Phase 1: Minimize Total Capacitance
(PGR-P1)
Modify the objective to minimize total capacitance
Modify the third constraint to calculate the total capacitance Ce per edge
  mq and rq are the slope and offset for the total edge capacitance respectively

## Slide 19: Phase 2: Minimize Total Power
From the phase 1 solution , we can obtain an “effective” utilization for each edge
Similarly, we can also obtain “unit capacitance” for each edge (i.e., capacitance of one wire on one edge) based on the solution of phase 1

## Slide 20: Phase 2 : Minimize Total Power
(PGR-P2)
Incorporate net activity and voltage level in the objective function to minimize total power directly
  get estimated edge capacitance for each edge from phase 1, and consider it to be constant
  but penalize the edge capacitance if over-utilized

## Slide 21: Solving PGR1 and PGR2*
Based on one set of initial route
Solve LP, get dual sol.
Identify new routes for each net
Setup edge weight
Have new routes?
Solve IP
yes
no
Price
Identify “promising” routes for each net by solving iterative LP relaxations via column generation
Branch
Solve IP via branch and bound
* [Wu, Davoodi, Linderoth, DAC’09, TCAD’11]
Wirelength optimized solution
Power-aware edge weights
Notes: Change font color

## Slide 22: Power-Aware Route Generation
Edge weights represent rate of improvement in objective
  i.e., capacitance in PGR1 and power metric in PGR2 from previous round of LP
Weighted shortest path finds additional candidate routes to improve the objective
  applied by replacing branches in an existing route from a previous LP iteration
ta
tb
0.85
0.85
0.07
0.04
0.12
0.17
0.06
0.07
0.07
t'a
tb
0.85
0.85
0.07
0.04
0.00
0.00
0.00
0.07
0.00
0.03
0.10
0.11
ub
vb

## Slide 23: IP Decomposition*
*[Wu, Davoodi, Linderoth, DAC’09, TCAD’11]
(Before detouring)
(After detouring)
1
2
3
4
5
6
7
8
9
10
11
12

## Slide 24: Simulation Setup
Random net activity generation
  uniform distribution between 0.1 and 0.9
Two voltage levels 0.9 and 1.1V
Capacitance (area, fringe, coupling) for each layer from 45nm NANGATE library
  based on the given edge utilization, we estimated wire spacing at each global bin
Price-and-branch was solved using CPLEX 9.0
  submitted jobs via Condor to CS grid at UW-Madison

## Slide 25: Simulation Flow
Initial solution: NTHU-Route 2.0 [Chang et al ICCAD08]
Voltage island generation [Chu et al ICCAD06]
  timing analysis on ISPD08 benchmarks
Based on the voltage islands, inserted LCs
  considered available white space
  minimized number of LCs while trying to position them as close as possible to the sink terminals
Initial Global Routing Solution
Voltage assignment & Inserting level converter
Power-optimized Global Routing
Tolerable wirelength
degradation factor = 0

## Slide 26: Benchmarks
Benchmark | # nets | #LC | # SP
adaptec1 | 177K | 20K | 130
adaptec2 | 208K | 17K | 195
adaptec3 | 368K | 43K | 359
adaptec4 | 401K | 36K | 296
adaptec5 | 548K | 85K | 454
newblue1 | 271K | 16K | 195
newblue2 | 374K | 47K | 312
Benchmark | # nets | #LC | # SP
newblue4 | 531K | 79K | 462
newblue5 | 892K | 84K | 658
newblue6 | 835K | 91K | 532
newblue7 | 1647K | 72K | 670
bigblue1 | 197K | 26K | 152
bigblue2 | 429K | 43K | 275
bigblue3 | 666K | 60K | 453
bigblue4 | 1134K | 51K | 509
Note: newblue3 is an un-routable benchmark, and therefore we didn’t consider it in this simulation

## Slide 27: Simulation Results
Benchmark | Initial Solution |  |  | Phase 1 (%) |  |  | Phase 2 (%) |  | 
 | WL0 | C | P | -WL | -C | -P | -WL | -C | -P
adaptec1 | 54.2 | 953 | 432 | 0.05 | 11.70 | 8.57 | 0.07 | 15.48 | 16.17
adaptec2 | 53.0 | 750 | 337 | 0.12 | 10.34 | 6.93 | 0.14 | 14.57 | 15.13
adaptec3 | 132.7 | 2287 | 1057 | 0.01 | 11.51 | 8.67 | 0.34 | 13.55 | 13.94
adaptec4 | 123.0 | 1614 | 751 | 0.02 | 12.16 | 8.46 | 0.04 | 16.92 | 17.2
adaptec5 | 158.7 | 2543 | 1200 | 0.38 | 8,60 | 6.08 | 0.43 | 10.23 | 10.88
newblue1 | 47.0 | 612 | 319 | 0.11 | 13.39 | 9.87 | 0.22 | 17.45 | 18.4
newblue2 | 77.6 | 895 | 453 | 0.04 | 14.19 | 7.87 | 0.09 | 19.2 | 19.34

## Slide 28: Simulation Results
Benchmark | Initial Solution |  |  | Phase 1 (%) |  |  | Phase 2 (%) |  | 
 | WL0 | C | P | -WL | -C | -P | -WL | -C | -P
newblue4 | 133.7 | 1955 | 928 | 0.02 | 13.39 | 9.61 | 0.54 | 17.45 | 17.61
newblue5 | 234.7 | 3405 | 1470 | 0.89 | 11.55 | 6.75 | 0.86 | 14 | 13.47
newblue6 | 180.2 | 2835 | 1367 | 0.62 | 12.56 | 9.35 | 0.57 | 16.35 | 17.8
newblue7 | 360.2 | 5004 | 2202 | 0.01 | 15.12 | 11.2 | 0.17 | 19.63 | 20.93
bigblue1 | 57 | 1110 | 619 | 0.23 | 10.68 | 7.2 | 0.16 | 12.17 | 12.56
bigblue2 | 92.4 | 1284 | 561 | 0.14 | 11.64 | 7.86 | 0.1 | 14.76 | 14.33
bigblue3 | 133 | 1665 | 815 | 0.91 | 15.22 | 10.99 | 0.93 | 20.25 | 20.31
bigblue4 | 233 | 3007 | 1254 | 0.18 | 16.03 | 12.12 | 0.28 | 22.31 | 22.46

## Slide 29: Comparison - Wirelength
Chart: Wirelength (%)
| adaptec1 | adaptec2 | adaptec3 | adaptec4 | adaptec5
NTHU Route | 100 | 100 | 100 | 100 | 100
Phase1 | 99.95 | 99.88 | 99.99 | 99.98 | 99.62
Phase1+2 | 99.93 | 99.86 | 99.66 | 99.96 | 99.57
Since the wirelength degradation factor β was set to 0, no wirelength degradation was found over all benchmarks

## Slide 30: Comparison – Capacitance & Power
After phase 1, the total capacitance and power has significant saving of 12.5% and 8.77% respectively
After phase 2, we can get additional 4.8% on capacitance and additional 7.93% on power saving
Chart: Total Capacitance (%)
| a1 | a2 | a3 | a4 | a5
NTHU Route | 100 | 100 | 100 | 100 | 100
Phase1 | 88.3 | 89.66 | 88.49 | 87.84 | 91.4
Phase1+2 | 84.52 | 85.43 | 86.45 | 83.08 | 89.77
Chart: Total Power (%)
| a1 | a2 | a3 | a4 | a5
NTHU Route | 100 | 100 | 100 | 100 | 100
Phase1 | 91.43 | 93.07 | 91.33 | 91.54 | 93.92
Phase1+2 | 83.83 | 84.87 | 86.06 | 82.8 | 89.12

## Slide 31: Conclusions
Proposed an IP formulation to minimize an interconnect power metric for global routing in multi-supply voltage domain
  implemented as a two-phase approach to handle the nonlinearity in the IP formulation
  price-and-branch procedure to systematically generate routes to reduce interconnect power
One-time optimization in the design flow, in effect achieves a balance in spreading congestion and rerouting nets to lower layers
  without over-usage of each routing resource
  without increase in wirelength

## Slide 32
Thank You
Notes: 32